## Slide 1: SoK: Limitations of Confidential Computing via TEEs for High-Performance Compute Systems
Ayaz Akram (yazakram@ucdavis.edu),
Venkatesh Akella, Sean Peisert, Jason Lowe-Power

## Slide 2: Summary
We analyze existing trusted execution environments (TEEs)
to categorize them based on their characteristics
to find out the underlying principles current TEEs rely on
to find out if the existing TEEs are a good fit for HPC style systems
Current TEEs are not a good fit for HPC
large application modifications or large TCB
focus on core-level execution
inconsideration of side channels
We present a few research directions to build HPC-focused TEEs

## Slide 3: Outline
What is confidential computing and secure HPC?
Requirements of an HPC-centric trusted execution environment?
Do existing TEEs work for HPC?
Way forward?

## Slide 4: What is Confidential Computing?
Confidential computing enables protection of "data in use"
mainly enabled by trusted execution environments (TEE)
TEEs provide
hardware-enforced isolation
cryptographic attestation to verify execution
no significant usability challenges
Other
Apps.
Physical memory
Secure
App.
OS
Zone of trust
data in use
C
C
Trusted Execution Environment
Examples of TEEs
KeyStone

## Slide 5: What is Secure HPC?
Lots of sensitive data
  Health data Personally identifiable information Proprietary data
Want to give easy access to scientists
Need high performance compute without trusting platform provider1
1 Sean Peisert, "Security in high-performance computing environments", CACM, 2017.

## Slide 6: Simplified threat model
Data
provider
Data
scientist
Other
users
Open
data
Trusted
Untrusted
Untrusted
Zone of trust
Compute provider
Physical memory
Secure
app
Operating system
or hypervisor
TEE
Encrypted
data
Unsecured
data
Runtime
or OS
Normal
app
Normal
app
Trusted Execution Environments

## Slide 7: Outline
What is confidential computing and secure HPC?
Requirements of an HPC-centric trusted execution environment?
Limitations of existing TEEs for HPC?
Way forward?

## Slide 8: What are the requirements of an HPC focused TEE?

## Slide 9: Requirements for an HPC-centric TEE
Minimal performance penalties for HPC-style workloads
    heavily multi-threaded and large working sets
Not require app. modifications or linking against special libs
Not require OS to be a part of the TCB
Capable of expanding across multiple compute nodes and other processing elements

## Slide 10: Outline
What is confidential computing and secure HPC?
Requirements of an HPC-centric trusted execution environment?
Do existing TEEs work for HPC?
Way forward?

## Slide 11: Do existing TEE technologies fit HPC environments?

## Slide 12: We need to look at the TEE primitives of today to see if the HPC TEE requirements are fulfilled!

## Slide 13: Primitives used by TEEs
Page table entry metadata
  Examples include Intel SGX, AMD SEV
Encryption of physical memory
Examples include Graviton, AMD SEV, ARM RME
Physical memory isolation via ISA extensions
Examples include RISC-V PMP used by Keystone, TIMBER-V
New privileged layers
Can be hardware /software (e.g., ARM RME, CURE)
Use of tags and identifiers
  Examples include ARM TrustZone, SiFive WorldGuard

## Slide 14: These primitives impose limitations on TEEs!

## Slide 15: Limitations of current TEEs
Heavy application code modifications
  limited support for traditional C libs
Large TCB
  entire guest OS in enclave
Focus on core-level execution
Other limitations
  fragmentation
  scalability
  data movement

## Slide 16: Requirements for an HPC-centric TEE
Minimal performance penalties for HPC-style workloads
  heavily multi-threaded and large working sets
Not require app. modifications or linking against special libs
Not require OS to be a part of the TCB
Capable of expanding across multiple compute nodes and other processing elements

## Slide 17: Outline
What is confidential computing and secure HPC?
Requirements of an HPC-centric trusted execution environment?
Do existing TEEs work for HPC?
Way forward?

## Slide 18: What is the way forward?

## Slide 19: Simplified view of a modern HPC system
Core
System view today
OS
App.
Memory
OS
App.
App.
Core … Core
Th0 … ThN
Acc.
Mem.
App.
Mem.
Local node Accelerator Remote node
Current TEEs can help create silos for individual components

## Slide 20: Our vision of a trusted modern HPC system
Trusted system view
Memory
App.
Core
App.
App.
Acc.
Core
Local node Accelerator Remote node

## Slide 21: Our vision of a trusted modern HPC system
Trusted system view
Memory
App.
Core
App.
App.
Acc.
Core
Local node Accelerator Remote node
No OS in TCB
Inclusive trusted components view

## Slide 22: Our vision of a trusted modern HPC system
Trusted system view
Memory
App.
Core
App.
App.
Acc.
Core
Local node Accelerator Remote node

## Slide 23: Our vision of a trusted modern HPC system
Trusted system view
Memory
App.
Core
App.
App.
Acc.
Core
Local node Accelerator Remote node
This is what we want!
1) for security
And, also
2) for performance

## Slide 24: Promising research directions
New hardware primitives
Horizontal privilege levels
Data centric enclaves
Capability based enclaves

## Slide 25: Summary
We analyze existing trusted execution environments (TEEs)
to categorize them based on their characteristics
to find out the underlying principles current TEEs rely on
to find out if the existing TEEs are a good fit for HPC style systems
Current TEEs are not a good fit for HPC
large application modifications or large TCB
focus on core-level execution
inconsideration of side channels
We present a few research directions to build HPC-focused TEEs

## Slide 26: Acknowledgment
We acknowledge the support of the following entities
  Director, Office of Science, Office of Advanced Scientific Computing Research, of the U.S. DOE under Contract No. DE-AC02-05CH11231.
  National Science Foundation under Grant No. CNS1925724.
  Anonymous reviewers for their valuable feedback.

## Slide 27: Thanks for listening!
Questions?

## Slide 28: SoK: Limitations of Confidential Computing via TEEs for High-Performance Compute Systems
Ayaz Akram (yazakram@ucdavis.edu),
Venkatesh Akella, Sean Peisert, Jason Lowe-Power